## Slide 1: Mixed-Integer Linear Programming
Computational Optimization
Instructor: Fengqi You
Cornell University

## Slide 2: Textbook
L.A. Wolsey, Integer programming. Wiley, 1998.
L.T. Biegler, I.E. Grossmann, A.W. Westerberg, Systematic Methods of Chemical Process Design. Prentice Hall Press, 1997.

## Slide 3: Mixed-Integer Linear Programming
Objective function and all constraints are linear
Some variables are continuous, and some are discrete/integer
Gomory (1958), Balas (1962), Dakin (1965), Nemhauser (1999)
x1
x2

## Slide 4: General Mixed-Integer Linear Program
There are no y variables ⇒ Linear Programming (LP)
There are no x variables ⇒ (pure) Integer Programming (IP)
We have both x and y ⇒ Mixed-Integer Linear Programming (MILP)
A general integer n ∈{0, 1, 2, 3, …N} can be modeled via binary variables yk:
or
Fewer 0-1 variables
Weaker relaxation

## Slide 5: Outline
Applications of MILP
  Synthesis of energy systems
  Reaction and conversion pathway/network analysis
  Scheduling of batch manufacturing processes
  Capacity planning of process networks
  Unit commitment for electric power systems operations
  Hospital operating room assignment and scheduling
Theory & Algorithm:
  Branch-and-bound algorithm
  Valid inequalities and cutting planes
  Disjunctive programming and logic optimization
Computational Issues

## Slide 6: Project Selection
A company is thinking about building new facilities in LA and SF.
Total capital available for investment: $10M
Question: Which facilities should be built to maximize the total profit?
 | capital needed | expected profit
1. factory in LA | $6M | $9M
2. factory in SF | $3M | $5M
3. warehouse in LA | $5M | $6M
4. warehouse in SF | $2M | $4M

## Slide 7: Project Selection
Define decision variables (i = 1, 2, 3, 4):
Then the total expected benefit: 9y1+5y2+6y3+4y4
the total capital needed: 6y1+3y2+5y3+2y4
Summarizing, the IP model is:
max 9y1+5y2+6y3+4y4
s.t. 6y1+3y2+5y3+2y4  10
yi {0,1}

## Slide 8: Modeling Discontinuous Domains and Functions
Discontinuous Domain
Discontinuous Function
0 L U
0 L U x
c

## Slide 9: Process Planning
Data
  To produce 1 lb of product B, 1.4 lb of material A is required
  A: cost $0.15/lb, maximum availability = 80,000,000 lb/year
  B: price $0.35/lb, maximum demand = 50,000,000 lb/year
  Process operating cost: $0.06/lb of B produced
  Process investment cost
    Fixed charge: $4,000,000/year
    Variable cost: $0.01/lb/year of B
Question: should the plant be built? If so, at what capacity?
Process
Material A
Product B
1.4 lb
1 lb

## Slide 10: Model
Variables:
  x1: amount of A consumed per year (million lb)
  x2: amount of B produced per year (million lb)
  y: 0-1 variable; equals to 1 if the process installed; 0, otherwise
Annual profit = 0.35x2 – 0.15x1 – (4y + 0.01x2) – 0.06x2
  sales raw material investment operations
Model:
Can the 2nd constraint be replaced by ?

## Slide 11: Exercise
Mass balance:
    To produce 1 lb of product B, 1.4 lb of material A is required
    To produce 1 lb of product C, 1.2 lb of material A is required
    A: cost $0.15/lb, maximum availability = 80,000,000 lb/year
    B: price $0.35/lb, maximum demand = 50,000,000 lb/year
    C: price $0.30/lb, maximum demand = 80,000,000 lb/year
Cost data: Process I Process II
    Operating cost $0.06/lb of B $0.05/lb of C
    Investment fixed cost $4,000,000/year $5,000,000/year
    Investment variable cost $0.01/lb/year of B $0.02/lb/year of C
Which plant(s) should be installed? At what capacity?
Process I
A
1.4 lb of A
1 lb of B
Process II
1 lb of C
1.2 lb of A

## Slide 12: Process Network

## Slide 13: Extension to Process Network
Mass balance
  i for process, j, j’ for chemicals
  Mi is a set for main product
  W is a variable for production amt
  μ is a parameter for mass balance
Capacity & Installation
  Q is a variable for capacity
    QU and QL are parameters for upper and lower bounds
  y is a 0-1 variable for installation

## Slide 14: Extension to Multi-Period Capacity Planning
Consider a number of time periods
  Capacity of a process can be expanded in each time period
  Consider the balance of capacity level, subject to budget constraint
  QE is a variable for the capacity expansion level at each time period
  Q is a variable for the capacity at each time period
  α and β are parameters for variable / fixed costs of capacity expansion
  CI is a parameter for the budget limit of each time period

## Slide 15: Mixed 0-1 Quadratic term (Glover’s Linearization)
For a nonlinear (quadratic) term p = x ∙ y, where x , L ≥ 0, and y {0, 1}
  It implies that
An equivalent MILP reformulation is:
If L = 0 and U = M, then we have the “big-M” formulation:
What if the product term p = y1 ∙ y2, where y1, y2 {0, 1}?

## Slide 16: Modeling Absolute Value Terms
An absolute value term z = |x|, where x , L < 0 < U and z ≥ 0.
  This is continuous but non-differentiable at x = 0.
It can be reformulated to a set of MILP inequalities
Introduce new variables x1 ≥ 0, x2 ≥ 0, and y {0, 1}

## Slide 17: Why absolute value? Example: Ridge & LASSO
Ridge Regression: LASSO:
LASSO (l1 penalty) results in sparse solutions – vector with more zero coordinates
Good for high-dimensional problems – don’t have to store all coordinates!
θ with
constant
l1 norm
θ with
constant
l0 norm
Ideally l0 penalty, but optimization becomes non-convex
θ with constant J(θ)
(level sets of J(θ))
θ with
constant
l2 norm
θ2
θ1

## Slide 18: Modeling with Integer Variables
Multiple Choices
  At least one Exactly one At most one
Implication
  If select i then select k Select i if and only if select k
Integer Number
Also
Fewer 0-1 variables
Weaker relaxation

## Slide 19: Modeling General Integer Variables with Binaries
One and only one y is selected
n = 0, 1, 2, …, N
n = 0, 1, 2, …, 2N+1-1
Fewer 0-1 variables
Weaker relaxation

## Slide 20: Knapsack Problem
We are given n items to be packed in a knapsack
Each item i ∈{1, 2, …n} has a value Pi and a weight Wi
The capacity of the knapsack is Q
The goal is to choose the items that fit in the knapsack with the max value.
Define:
  yi = 1 if item i is chosen
  If we had multiple resources j ∈{1, 2, ..m} (e.g. weight, volume, etc.) with capacities Qj, we would replace the capacity constraint with:
Capacity Constraint

## Slide 21: Example of Knapsack Problem
Given below item weight and market value of the items. How to maximize the market value earned of items by placing some or all of them into the knapsack with a capacity?

## Slide 22: Set Covering Problem
We are given n tasks to be covered by m<n machines.
Each machine j ∈{1, …m} can carry out a subset of tasks Ij⊂I = {1, 2, …, n}
The compatibility is represented via parameter: Aij = 1 if i ∈ Ij
The cost of a machine is Cj
The objective is to find the set of machines that covers all tasks with the minimum cost
Define:
  yj = 1 if machine j is chosen
NP-hard problem
…
…
Task i Machine j
1
2
3
4
n
1
2
3
4
m

## Slide 23: Set Covering Example: Location of Fire Station
Fire station(s) can be placed in any of the 11 neighborhoods
  A fire station can handle the fires for both its neighborhood and any adjacent neighborhood (any neighborhood with a non-zero border with its home neighborhood).
Minimize the total number of fire stations
  Another example: Cell tower coverage
    http://examples.gurobi.com/cell-tower-coverage/

## Slide 24: Assignment Problem
We are given n tasks and n machines
Each task i ∈{1, 2, …, n} has to be assigned to a machine j ∈{1, 2, …, n}
The cost of assignment is Cij
The objective is to find the assignment with the minimum total cost
Define:
  yij = 1 if task i is assigned to machine j
  If solved as LP, there is always an optimal solution with integral values
…
…
1
2
3
4
n
1
2
3
4
n
Task i Machine j

## Slide 25: Traveling Salesman Problem
There are n cities to be visited exactly once by a traveling salesman
The distance/cost from city i to city j is Cij
The objective is to find the sequence of cities that yield the minimum total distance/cost
Define:
  yij = 1 if we visit city i before city j
Constraint:
  Enter/exist each city once and only once
Subtour elimination constraint
An NP-complete problem
http://examples.gurobi.com/traveling-salesman-problem/

## Slide 26: Example of TSP Subtours
1
2
3
5
6
4
1
2
3
5
6
4

## Slide 27: Traveling Salesman Problem Applications
Transportation: school bus routes, service calls, delivering meals / mailing (USPS, FedEx, UPS …)
Manufacturing: an industrial robot that drills holes in printed circuit boards, making multiple grades of polymers in a reactor …
Others: planning new telecommunication networks, genome sequencing (arranging DNA fragments in sequence)
This tour of 13,500 US cities was generated by an advanced algorithm that used several “tricks” to limit the number of possible tours (using 5 CPU-years)
http://www.tsp.gatech.edu

## Slide 28: Facility Location Problem
There are n facilities (plants) and m customers
  We want to decide how to satisfy customer demand
  Which new facilities to build
  How much to produce and ship
Parameters
  The capacity of facility i ∈{1, 2, …, n} is Ai
  The cost of setting up facility i ∈{1, 2, …, n} is Fi
  The cost of shipping products from i to j is Cij
  The demand of customer j ∈ {1, 2, …, m} is Dj
Variables
  xij = amount shipped from i to j
  yi = 1 if we set up (install) facility i
http://examples.gurobi.com/facility-location

## Slide 29: Operating Room Assignment/Scheduling
Limited number of operating rooms
Hospital needs to schedule the assignment of operating rooms to different departments weekly.
Challenges:
  Operating rooms are staffed in 8 hour blocks.
    If there are 10 operating rooms staffed Monday – Friday, then total would be 400 hours/week to assign
  Each operating room is assigned to at most one department per day
  Each department sets their own target number of allocation hours, which may not be integer.
  Departments may have daily and weekly requirements, e.g.
    Ophthalmology needs at least 2 operating rooms per week
    The oral surgeon is only present on Tuesdays and Thursdays.

## Slide 30: Operating Room Assignment/Scheduling
Decisions: Integer variables xit represent the number of operating rooms department i is allocated on day t
  How many ORs to assign each department on each day
  with index i for departments and index t for day
Objective: Maximize the percentage of target allocation hours that each department is actually allocated
  Surgeons are frequently paid on a fee-for-service basis, so changing allocated operating rooms directly affects their income.
  The schedule must strike a delicate balance between all the surgical departments in the hospital  highly political.
  Example: If otolaryngology department has a target of 37.3 hours per week and was allocated 4 operating rooms for a week, then their percentage of target allocation hours = (8 × 4) ÷ 37.3 = 85.8%
  If target allocation hours are Ti for department i, then maximize the sum of (8 × xit) ÷ Ti over all departments and days of the week.

## Slide 31: Operating Room Assignment/Scheduling
Constraints
  At most N operating rooms are assigned every day
  The number of operating rooms allocated to a department on a given day cannot exceed the number of surgery teams that department has available that day
  Meet department daily/weekly minimums and maximums
Parameters
Ti target allocation hours of department i
N maximum available operating rooms
Ait number of available surgery teams of department i on day t
DLit minimum number of operating rooms required by department i on day t
DUit maximum daily requirement
WLi maximum number of operating rooms required by department i of the week
WUi maximum weekly requirement

## Slide 32: Case study: Mount Sinai Hospital
Assigning 10 operating rooms (400 hours/week) to 5 dept.
Department | Weekly Target Allocation Hours
Ophthalmology | 39.8
Gynecology | 118.2
Oral Surgery | 19.9
Otolaryngology | 37.3
General Surgery | 189.7
Department | M | T | W | R | F
Ophthalmology | 2 | 2 | 2 | 2 | 2
Gynecology | 3 | 3 | 3 | 3 | 3
Oral Surgery | 0 | 1 | 0 | 1 | 0
Otolaryngology | 1 | 1 | 1 | 1 | 1
General Surgery | 6 | 6 | 6 | 6 | 6
Department | Minimum | Maximum
Ophthalmology | 3 | 6
Gynecology | 12 | 18
Oral Surgery | 2 | 3
Otolaryngology | 2 | 4
General Surgery | 18 | 25
Available Surgery Teams
Weekly Requirements by Dept.

## Slide 33: Revisited: Economic Dispatch
Sets
I set of generators indexed by i
J set of generators indexed by j
Variables
gi power output of generator i
wj power injection from wind farm j
Parameters
CGi unit production cost of generator i
CWj unit power cost of wind farm j
D demand
Gmini minimum output of generator i
Gmaxi maximum output of generator I
WFj power forecast of wind farm j
All generators must be dispatched over the minimum power output limit – might lead to absurd decisions or extra cost

## Slide 34: Unit Commitment (single period)
Introducing binary 0-1 variable ui to model the on/off decisions for each thermal generation unit i
  Allowing the power output of a generator to be zero ( at “off” status)
Load
Time
12
6
0
18
24
Unit 1
Unit 2
Unit 3

## Slide 35: Multi-Period Unit Commitment with Renewables
Extend to a multi-period planning/scheduling model
  Add set T indexed by t for time periods
  Model dynamic/time-dependent unit commitment decisions
  Account for start-up and shutdown decisions/costs
Binary 0-1 Variables
sit equal to 1 if generator i is turned on at time t ; otherwise, sit =0.
fit equal to 1 if generator i is shut down at time t ; otherwise, fit =0.
Parameters
SUi start-up cost of generator i
SDi shut down cost of generator i

## Slide 36: Additional Considerations on Unit Commitment
Minimum up/down-time constraints
  Once a unit is started/shut-down, it should be on/off for at least a minimum up/down time before it can be shut-down/re-started.
Security on ramp up and ramp down of units
  To avoid damaging the turbine, the electrical output of a unit cannot change (i.e. increase/decrease) by more than a certain amount over some time
Reserve
  Rapid increase in production in case of unacceptable frequency drop due to unanticipated loss of a generating unit
  Protect the system against “credible outages”
  Types: (a) Increase output when generation < load, (b) Pumped hydro plants, (c) Demand reduction (e.g. voluntary load shedding)
Emission constraint/penalty

## Slide 37: Security-Constrained Unit Commitment (SCUC)
Continuous Variables
rit reserve of generator i at time t
Parameters
Cui no-load cost of generator i
MUi minimum up time of generator i
MDi minimum down time of generator i
RDit ramp down rate of generator i at time t
RUit ramp up rate of generator i at time t
Rmint system reserve requirement of time t
Rmaxit reserve capacity of generator i, time t

## Slide 38: MILP Applications in Systems Engineering
Systems Design:
  Selection of equipment units (e.g. distillation vs. extraction) ‐ Superstructure optimization
  Selection of equipment sizes
  Matching in heat exchanger networks (hot ↔ cold pairs)
Systems Operations:
  Decision to expand/retrofit a process
  Scheduling of batch and continuous processes
Systems Control:
  Selection of linearized model for MPC
  On/off control action
Systems Biology
  Gene addition and/or knock‐out

## Slide 39: Discrete Decisions in Process Design
Example: What is the best way to produce Vinyl Chloride Monomer? (Turkay & Grossmann, 1998)
Optimization Decisions:
  Distillation sequence (discrete), Sizing (discrete or continuous), Operating conditions (continuous)

## Slide 40: Synthesis of Distillation Sequences
Example: Separate mixture of A (lightest), B, C, D (heaviest) into pure components using sharp separation
Superstructure
Fi flows
yi existence columns

## Slide 41: Assumption: Perfect Recoveries

## Slide 42: Example: Split Fraction
Can work with total flows
Notes: In general terms, the problem can be stated as follow: we are given a PSCN,
as shown in the screen, it includes the suppliers, customers, plant sites and the transportation links between them. The investment cost and transportation costs are expressed by a fixed charge function.
As shown here. The transportation time and the supply and demand constraints are also given.

## Slide 43: Input Parameters

## Slide 44: MILP Model

## Slide 45: Optimal Solution

## Slide 46: General Problem Statement
Given:
  A multicomponent mixture tend to be separated into pure products
  Find a minimum cost separation sequence
Assumptions:
  Simple columns
  Fixed pressure
  Sharp splits and Perfect recoveries
  Adjacent key components for separation given inlet components
  Since 100% recovery assumed no need to “duplicate” columns (eg. A/B, B/C, C/D)
  Heat duties of condenser and reboiler as
  Kc, KR are constants for fixed reflux ratios
Investment
Utility
Notes: In general terms, the problem can be stated as follow: we are given a PSCN,
as shown in the screen, it includes the suppliers, customers, plant sites and the transportation links between them. The investment cost and transportation costs are expressed by a fixed charge function.
As shown here. The transportation time and the supply and demand constraints are also given.

## Slide 47: General Model
For Col k, let
Define
    Set of intermediate products IP = {m}, e.g., IP = {(ABC), (AB)}
    COL = {k}
    FSF = {col k have as feed initial mixture} e.g. 1,2,3
    FSm = {col k have as feed intermediate m} e.g. 4->10
    PSm = {col k produce intermediate m} 1->7 (BCD Col 1)

## Slide 48: MILP Model for Distillation Sequence
Model
Note: Generally KRK = KCK
Notes: In general terms, the problem can be stated as follow: we are given a PSCN,
as shown in the screen, it includes the suppliers, customers, plant sites and the transportation links between them. The investment cost and transportation costs are expressed by a fixed charge function.
As shown here. The transportation time and the supply and demand constraints are also given.

## Slide 49: Olefin Separation System (BP)
Goal: Synthesize optimal separation system

## Slide 50: Process Superstructure

## Slide 51: Optimal Solution (Successful Story)

## Slide 52: Conversion Network Analysis and Optimization
Diverse pathways in a conversation/reaction networks from raw materials to final products
Example: Bioconversion network
8 biomass feedstocks
Hundreds of “known” conversion technologies
4 types of biofuels + 19 bioproducts

## Slide 53: “Optimal Pathways” from Bioconversion Network
Help to identify:
Optimal production pathways for a given demand of product
Optimal utilization pathways for a given supply of feedstock
Optimal pathways for a given feedstock and product
Example network size
200 conversion technologies
142 feeds/intermediates/products

## Slide 54: Optimal Pathway/Technology Selection Model
Minimize total annualized cost (CAPEX + OPEX)
  Subject to mass balance, production capacity, availability and demand
Sets
I set of feedstocks/intermediate/products indexed by i
J set of technologies/processes indexed by j
Binary 0-1 Variables
yj selection of technology/process j
Continuous Variables
pi purchase amount of product i
si sale amount of material/product i
qj capacity of process with technology j
wj production level of process with technology j

## Slide 55: Optimal Pathway/Technology Selection Model
Sets
I set of feedstocks/intermediate/products indexed by i
J set of technologies/processes indexed by j
Parameters
f(∙) nonlinear function for capital cost
Ai maximum availability/supply of material/product i
Di demand of product i
CPi unit procurement cost of product i
CWi unit production cost of product i
QLj minimum process capacity level of process with technology j
QUj maximum process capacity level of process with technology j
Mi, j conversion coefficient of product i in process with technology j

## Slide 56: Optimal Pathway/Technology Selection Model
Use piecewise linear approximation to model nonlinear function f (qj), and formulate the problem as an MILP
Capacity limitations
Production is limited to capacity
Mass balance
Availability constraint
Demand constraints

## Slide 57: Piecewise Linear Function (Nonlinear)
Suppose the piecewise linear function f (x) has break points B0, B1, …, Bp

## Slide 58: Example Solution

## Slide 59: Batch Processing
Batch Process: more than ¼ of global production
  Specialty and performance chemicals
  Electronic/agricultural materials, metals
  Pharmaceutical ingredients, biochemicals
  … …
Features
  Sequence-dependent control policy
  Unsteady state operations
  Highly depend on manual operations
Production scheduling is the key issue
  What to be produced?
  How much to be produced?
  When/ in what order the batches are produced?
  Which equipment to be produced?

## Slide 60: State Task Network (STN) (Kondili, Pantelides, Sargent, 1993)
I1
Heat
Reaction1
Separation
Reaction 3
I2
I3
P1
P2
I4
Reaction2
1h
0 1 2 3 4 5 6 Time (h)
Reactor 1
Reactor 2
Reactor 3
Column
Reaction 2
Reaction 3
Separation
Reaction 1
Heating
M1
3 materials
(M1, M2, M3)
2 products
(P1, P2)
M2
M3

## Slide 61: Discrete Time Formulations
Main Assumptions
  The scheduling horizon is divided into a finite number of time intervals with known duration
  Tasks can only start or finish at the boundaries of these time intervals
Advantages
  Resource constraints are only monitored at predefined/fixed time points
  Simple models and easy representation of various scheduling features
Disadvantages
  Model size and complexity depend on the number of time intervals
  Constant processing times are required (rounding may be suboptimal)
  Changeovers are difficult to handle
Discrete Time Representation

## Slide 62: Basics of MILP: Relaxation
General MILP problem (MILP)
  For general integer , use
Replacing the integrality requirement y∈{0,1} with y∈[0,1] leads to a relaxation (R-MILP), which is an LP:

## Slide 63: Basics of MILP: Relaxation
Relaxation leads to a better objective value
  Larger for max. problem and smaller for min. problem
  In general, a relaxation of a problem is obtained by removing constraints (i.e. expanding the feasible region)
(MILP)
(R-MILP)

## Slide 64: Relaxation Principle
Let Problem 1:
Problem 2:
If (i.e. ) and , then
Proof:
  is a relaxation of (why?), so
  Because is a feasible solution of Problem 2 and , it is easy to show that it is also a feasible solution of Problem 1 (why?) and hence (why?)
  We can conclude that (why?)
  Since is shown to be a feasible solution of Problem 1 and , is the optimal solution of both problems. (why?)

## Slide 65: Constraint Generation – TSP as An Example
An alternative formulation of TSP
Given a network with n cities to be visited exactly once by a traveling salesman
This is a complete undirected graph G = (N, E)
N = {1, 2, …, n}, E is the set of edges for every possible pair of different nodes i and j, say .
The distance from city i to city j is Cij, or Ce.
Define: xe = 1 if edge e is used in the selected tour
Objective: Find a tour w/ minimum total distance.
Degree constraints: Each node i should be connected to exactly two selected edges.
  δ(i) is the set of edges connecting to node i
Cut constraints: Eliminating subtours
  δ(S) is the set of edges in the cut that have one endpoint in S, and one endpoint in N-S

## Slide 66: Example of TSP Formulation
Degree constraint: each node connects to two selected edges
  e.g. Node 1 connects to {1, 5} and {1, 2} – note that all edges are undirected
Cut constraint: each node connects to two selected edges
  e.g. S = {1, 2, 3}, N-S = {4, 5, 6}, then the following graph violates the cut constraint (why rhs is 2 instead of 1)?
1
2
3
5
6
4
1
2
3
5
6
4

## Slide 67: Solving TSP with LP-based Constraint Generation
Solving the LP relaxation of the TSP problem with only the degree constraints:
Check if the solution satisfies the cut constraints below. If no constraint is violated, the current solution is optimal. If a violated constraint is found, add it to the LP problem above, and re-solve this “updated” LP, i.e. constraint generation.

## Slide 68: Solving TSP with LP-based Constraint Generation
Starting from a solution from the TSP-LP problem (with degree constraints only plus newly added “violated” constraints), let’s denote it as x*.
How to check if x* satisfies the cut constraint?
Formulate it as a minimum-cut problem!
  Take the complete graph G = (N, E), and build a directed graph D as follows: for each undirected edge {i, j} include two directed edges (i, j) and (j, i) and give each of these two edges the capacity x*{i, j}. Let node 1 be the source node. Then, for each node t = 2, 3, …, N, let t be the sink node, and fund the minimum cut separating node 1 and node t in D (e.g. using the Ford-Fulkerson algorithm); if the resulting minimum cut (S, N-S) (where and ) has capacity less than 2, then S gives a cut constraint that is violated by x*. If the minimum cut for every t = 2, 3, …, N has capacity at least 2, then all cut constraints are satisfied.

## Slide 69: Example of TSP
An “optimal” solution from solving the LP relaxation of TSP with degree constraints only
  Solid blue lines are for xe = 1; Dash yellow lines are for xe = 0.5;
If choose S = {1, 2, 3}, then the flow capacity is 1, which is less than 2.
The Separation Procedure could find this cut when choose node 4 as the sink.
1
2
3
5
6
4

## Slide 70: What is the Optimal solution of a 2-Variable IP?
maximize 3x + 4y
s.t. 5x + 8y  24, x, y  0 and integer
0 1 2 3 4 5
0 1 2 3 4 5
Question: What is the optimal integer solution?
What is the optimal linear solution?
Can one use linear programming to solve the integer program?

## Slide 71: A Rounding Technique Might NOT Be Useful
Solve LP (ignore integrality) get x=4.8, y=0 and z =14.4
Round, get x=5, y=0, infeasible!
Truncate, get x=4, y=0, and z =12
Same solution value at x=0, y=3
Optimal is x=3, y=1 and z =13
maximize 3x + 4y
s.t. 5x + 8y  24, x, y  0 and integer
0 1 2 3 4 5
0 1 2 3 4 5

## Slide 72: Another Example
LP Optimal
x1 = 5 7/16
x2 = 2 11/16
Round up?
x1 = 6
x2 = 3
Round off?
x1 = 5
x2 = 3
Round down?
x1 = 5
x2 = 2
LP relaxation, then round off ?
max z = 3 x1 + 4 x2
s.t. 2x1 + 6 x2  27
x2  2
3x1 + x2  19
x1 , x2  0 and Integer
IP Optimal
x1 = 4
x2 = 3

## Slide 73: The Mystery of Integer Programming
Integer variables make an optimization problem much more difficult to solve. Memory and solution time may rise exponentially as more integer variables are added
  Some integer programs are easy (millions of variables)
  Some integer programs are hard (some problem with only 100 variables that have never been solved to optimality)
  many combinations of specific integer values for the variables must be tested, and each combination requires the solution of a "normal" LP. The number of combinations can rise exponentially with the size of the problem.
Solvers for integer programs are extremely sensitive to the formulation. (not true for LPs)
  There are often multiple ways of modeling the same integer program, where integer variables can be used to model yes/no decisions

## Slide 74: Solution Techniques for Integer Programs
Enumeration
  Complete enumeration
    list all “solutions” and choose the best
    For n binary variables, there are 2n+1 nodes (subproblems).
  Branch and bound (Implicit enumeration by solving LPs)
    Implicitly search all solutions, but cleverly eliminate the vast majority before they are even searched based on bounds
    Solution process is for “closing the gap”
Cutting plane techniques
  Use LP to solve integer programs by adding constraints to eliminate the fractional solutions.
Branch-and-cut
  Branch and Bound with cutting planes

## Slide 75: Complete Enumeration
Systematically considers all possible values of the decision variables.
  If there are n binary variables, there are 2n different ways.
Iteratively break the problem in two. At the 1st iteration, we consider separately the case that x1 = 0 and x1 = 1.

## Slide 76: Complete Enumeration – Time Consuming
Suppose that we could evaluate 1 billion solutions per second. Let n = number of binary variables
Solutions times
  n = 30, 1 second
  n = 40, 17 minutes
  n = 50 11.6 days
  n = 60 31 years
Suppose that we could evaluate 1 trillion solutions per sec.
Solutions times
  n = 70, 1 second
  n = 80, 17 minutes
  n = 90 11.6 days
  n = 100 31 years

## Slide 77: Branch and Bound
Implicitly enumerate all possible integer solutions
  By solving a single subproblem, many possible solutions may be eliminated from consideration
Key idea:
  Search the enumeration tree, but at each node solve the linear program at the node and eliminate the subtree (fathom it) if
    The solution is integer (there is no need to go further) or
    The best solution in the subtree cannot be as good as the best available solution (for the current upper bound) or
    There is no feasible solution
If it is unnecessary to branch on a subproblem, we say that it is “fathomed”

## Slide 78: Branch-and-Bound Overview
Recursively solve linear program at each node by fixing the values/bounds of the integer variables
Fathom if (1) lower bound at node is larger than value of a known feasible solution (i.e. upper bound), (2) integer solution is found, or (3) LP is infeasible
x1 = 1
x1 = 0
x2 = 1
x2 = 0
x2 = 1
x2 = 0

## Slide 79: Example Problem
maximize 16x1 + 22x2 + 12x3 + 8x4 +11x5 + 19x6
subject to 5x1 + 7x2 + 4x3 + 3x4 +4x5 + 6x6  14
xj = 0, 1 for j = 1 to 6

## Slide 80: Node 1 is the original LP Relaxation
1
44 3/7
Solution at node 1:
x1 =1 x2 = 3/7 x3 = x4 = x5 = 0 x6 =1 z = 44 3/7
maximize 16x1 + 22x2 + 12x3 + 8x4 +11x5 + 19x6
subject to 5x1 + 7x2 + 4x3 + 3x4 +4x5 + 6x6  14
0  xj  1 for j = 1 to 6
The IP cannot have value higher than 44 3/7.

## Slide 81: Node 2 is the LP Relaxation plus constraint x1 = 0
2
x1 = 0
1
44 3/7
44
Solution at node 2: x1 = 0 x2 = 1 x3 = 1/4 x4 = x5 = 0 x6 = 1 z = 44
maximize 16x1 + 22x2 + 12x3 + 8x4 +11x5 + 19x6
subject to 5x1 + 7x2 + 4x3 + 3x4 +4x5 + 6x6  14
0  xj  1 for j = 1 to 6, x1 = 0

## Slide 82: Node 3 is the LP Relaxation plus constraint x1 = 1
2
x1 = 0
1
44 3/7
44
3
x1 = 1
The solution at node 1 was
x1 =1 x2 = 3/7 x3 = x4 = x5 = 0 x6 =1 z = 44 3/7
Note: it was the best solution with no constraint on x1. So, it is also the solution for node 3. (If you add a constraint and the old optimal solution is feasible, then it is still optimal)
44 3/7

## Slide 83: Node 4 is LP Relaxation plus constraints x1 = 0 & x2 = 0
4
x2 = 0
1
2
3
x1 = 0
x1 = 1
44 3/7
44
44 3/7
Solution at node 4: X = [ 0 0 1 0 1 1 ], z = 42
42
4
1
Our first integer solution!
  No further searching from node 4 because there cannot be a better integer solution
  No solution in the subtree can have a value better than 42

## Slide 84: Solve the LP’s at Nodes 5, 6, and 7
7
x2 = 1
4
x2 = 0
5
x2 = 1
1
2
3
x1 = 0
x1 = 1
44 3/7
44
44 3/7
42
6
x2 = 0
44
44
44 1/3
4
1
We would eliminate (fathom) a subtree if no solution in the subtree would be better than the upper bound (42).
  No new integer solutions were found.
  The integer solution is the best solution on hand.
  The current best bound is 42

## Slide 85: Solve the LP’s at Nodes 8 - 13
4
x2 = 0
6
x2 = 0
5
x2 = 1
13
x3 = 1
1
2
3
x1 = 0
x1 = 1
44 3/7
44
44 3/7
42
7
x2 = 1
44
44
44 1/3
8
x3 = 0
9
x3 = 1
10
x3 = 0
11
x3 = 1
12
x3 = 0
43.75
43.5
43.25
43.8
44.3
-
4
We have solved 13 different linear programs so far.
  One integer solution found, and one subtree fathomed (pruned) because the solution is integer (node 4) with a value of 42
  One subtree fathomed because the solution is infeasible (node 13) – why fathom the substree if the node is infeasible?

## Slide 86: Solve the LP’s associated with the Next Nodes
5
x2 = 1
1
2
3
x1 = 0
x1 = 1
44 3/7
44
44 3/7
4
x2 = 0
42
6
x2 = 0
7
x2 = 1
44
44
44 1/3
8
x3 = 0
9
x3 = 1
10
x3 = 0
11
x3 = 1
12
x3 = 0
13
x3 = 1
43.75
43.5
43.25
43.8
44.3
-
43.75
42.66
We can fathom the node with z = 42.66. Why?
  The bound at each node is obtained by solving an LP, but all variable are integer, and so the objective is integer
  If the best integer valued solution for a node is 42.66, then we know the best bound is at most 42, so do other bounds.

## Slide 87: Round Down All the Bounds
The best solution has value 42
5
x2 = 1
1
2
3
x1 = 0
x1 = 1
44
44
44
4
x2 = 0
42
6
x2 = 0
7
x2 = 1
44
44
44 1/3
8
x3 = 0
9
x3 = 1
10
x3 = 0
11
x3 = 1
12
x3 = 0
13
x3 = 1
43
43
43
43
44
-
43
42

## Slide 88: Solving More Nodes
43
42
43
43
5
x2 = 1
1
2
3
x1 = 0
x1 = 1
44
44
44
4
x2 = 0
42
6
x2 = 0
7
x2 = 1
44
44
44 1/3
8
x3 = 0
9
x3 = 1
10
x3 = 0
11
x3 = 1
12
x3 = 0
13
x3 = 1
43
43
43
43
44
-
43
42
We found a new integer solution!
x1 = 1, x2 = x3 = 0, x4 = 1, x5 = 0, x6 = 1 z = 43
The current best solution has value 43

## Slide 89: Fathom
1
2
3
x1 = 0
x1 = 1
44
44
44
4
x2 = 0
42
5
x2 = 1
6
x2 = 0
7
x2 = 1
44
44
44
8
x3 = 0
9
x3 = 1
10
x3 = 0
11
x3 = 1
12
x3 = 0
13
x3 = 1
43
43
43
43
44
-
8
9
10
11
If we had found this integer solution earlier, we could have saved some searching
The best integer solution has value 43

## Slide 90: Finishing Up
1
2
3
x1 = 0
x1 = 1
44
44
44
4
x2 = 0
42
5
x2 = 1
6
x2 = 0
7
x2 = 1
44
44
44
8
x3 = 0
9
x3 = 1
10
x3 = 0
11
x3 = 1
12
x3 = 0
13
x3 = 1
43
43
43
43
44
-
8
9
10
11
-
-
14
15
16
17
44
44
18
19
-
38
The best integer solution has value 43

## Slide 91: Lessons Learned
Branch and Bound can speed up the search
  Only 25 nodes (linear programs) were evaluated
  Other nodes were fathomed
Obtaining a good feasible solution earlier can be valuable
  only 19 nodes would have been evaluated
Solve linear programs faster, because we start with an excellent or optimal solution
  uses a technique called the dual simplex method
Obtaining better bounds can be valuable
  We sometimes use properties that are obvious to us, such as the fact that integer solutions have integer solution values

## Slide 92: Branch and Bound
Notation:
  z* = optimal integer solution value
  Subdivision: a node of the B&B Tree
  Incumbent: the best integer feasible solution on hand
  zI: value of the incumbent, i.e. the lower bound
  zLP: value of the LP relaxation of the current node, giving a upper bound
  Children of a node: the two problems created for a node, e.g., by saying xj = 1 or xj = 0
  LIST: the collection of active (not fathomed) nodes, with no active children
NOTE: zI  z*

## Slide 93: Illustrating the definitions
z* = 43 = optimal integer solution value. (We found it later in the search)
Currently best integer solution is 0 0 1 0 1 1 zI = 42. It is the optimal solution for the subdivision 4
The zLP values for each subdivision are next to the nodes
The best integer solution has value 42
4
x2 = 0
6
x2 = 0
5
x2 = 1
13
x3 = 1
1
2
3
x1 = 0
x1 = 1
44 3/7
44
44 3/7
42
7
x2 = 1
44
44
44 1/3
8
x3 = 0
9
x3 = 1
10
x3 = 0
11
x3 = 1
12
x3 = 0
43.75
43.5
43.25
43.8
44.3
-
4

## Slide 94: Illustrating the definitions
The children of node (subdivision) 1 are nodes 2 and 3. The children of node 3 are nodes 6 and 7
LIST = { 8, 9, 10, 11, 12 } = unfathomed nodes with no active children
4
x2 = 0
6
x2 = 0
5
x2 = 1
13
x3 = 1
1
2
3
x1 = 0
x1 = 1
44 3/7
44
44 3/7
42
7
x2 = 1
44
44
44 1/3
8
x3 = 0
9
x3 = 1
10
x3 = 0
11
x3 = 1
12
x3 = 0
43.75
43.5
43.25
43.8
44.3
-
4
The best integer solution has value 42

## Slide 95: Branch and Bound Algorithm
INITIALIZE LIST = {original problem} Best integer solution: =  zI = -
SELECT:
  If LIST = , then the current integer solution is optimal if it exists, and the problem is infeasible if no integer solution exists;
  else, let S be a node (subdivision) from LIST.
  Let xLP be the optimal solution to S
  Let zLP = its objective value
FATHOM & BRANCH
  Four cases
1
44 3/7
e.g., S = {1}

## Slide 96: Branch and Bound Algorithm
CASE 1. zLP = - (the LP is infeasible)
  Remove S from LIST (fathom), return to SELECT
  e.g., S = {13}
CASE 2. - < zLP  zI
  That is, the LP is dominated by the upper bound.
  Then remove S from LIST (fathom), return to SELECT
  e.g., the upper bound is 43, and node 14 is selected. zLP = 43
8
43
14
43
8
42
14
13
-
13

## Slide 97: Branch and Bound Algorithm
CASE 3. zI < zLP and xLP is integral
  That is, the LP solution is integral and dominates the incumbent and the current upper bound.
  Then Incumbent := xLP; zI := zLP
  Remove S from LIST (fathomed by integrality), return to SELECT
  e.g., node 4 was selected, and the solution to the LP was integer-valued.
CASE 4. zI < zLP and xLP is not integral
  There is not enough information to fathom S
  Remove S from LIST, add the children of S
  to LIST, return to SELECT
  e.g., select node 3.
44 3/7
6
x2 = 0
7
x2 = 1
3
x1 = 1
List := List – 3 + {6,7}
42
4
4

## Slide 98: Node Selection Rules
Depth-first Search:
  Always choose one of the new subproblems just generated; typically the one with the best lower bound
  Backtrack when node is discarded
  Advantages: can potentially find a (good) solution fast
  Disadvantages: “Hidden” good solutions difficult to find
Best-first Search:
  Always choose the subproblem with the best lower bound
  Advantages: examines potentially good nodes; uniformly tighten bounds
  Disadvantages: tree tends to be larger
Breadth-first Search:
  Expand all nodes at a level before going to the next
  Not used in practice

## Slide 99: Selection/ Branching Rules
Rule of Thumb 1: Don’t let LIST get too big (the solutions must be stored). So, prefer nodes that are further down in the tree – Depth-first Search
Rule of Thumb 2: Pick a node of LIST that is likely to lead to an improved the currently best solution. Sometimes heuristics are used to come up with a good feasible solution.
Rule of thumb 3: if it appears clear that xj = 1 in an optimal solution, it is often good to branch on xj = 0 vs xj = 1 The hope is that a subdivision with xj = 0 can be pruned
Rule of thumb 4: branching on important variables is worthwhile

## Slide 100: Branch and Bound for General Integer Program
Solving an IP with general integer variables n ∈{0, 1, 2, 3, …N}
Approach 1: A general integer n ∈{0, 1, 2, 3, …N} can be modeled via binary variables yk:
Approach 2: Generating subproblems by branching on an appropriately chosen fractional-valued variable
  Suppose a fractional value between the integers i and i+1. Then the two newly generated subproblems are
  New Subproblem 1 Old subproblem + Constraint xi ≤ i
  New Subproblem 2 Old subproblem + Constraint xi ≥ i + 1
or
Fewer 0-1 variables
Weaker relaxation

## Slide 101: Branch and Bound Example
X2
X1

## Slide 102: Branch and Bound Example
Bounding: solve linear programming relaxation:
Branching: divide into 2 subproblems:
X2
X1
upper = 59/7 ≈ 8.43

## Slide 103: Branch and Bound Example
Node selection: select (highest) right node
Bounding: solve linear programming relaxation: infeasible
Node is thus fathomed by infeasibility
X2
X1
infeasible
upper = 59/7 ≈ 8.43

## Slide 104: Branch and Bound Example
X2
X1
Node selection: select left node
Bounding: solve linear programming relaxation:
Branching: divide into 2 subproblems:
upper = 59/7 ≈ 8.43
upper = 7.5
infeasible

## Slide 105: Branch and Bound Example
Node selection: select (lowest) right node
Bounding: solve linear programming relaxation:
Node is thus fathomed by optimality
X2
X1
infeasible
upper = 59/7 ≈ 8.43
upper = 7.5
lower = 7
Integer solution (2, 1)

## Slide 106: Branch and Bound Example
upper = 6
infeasible
Node selection: select (lowest) left node
Bounding: solve linear programming relaxation:
Solution is 6, because 6<7 node is fathomed by bound
X2
X1
upper = 59/7 ≈ 8.43
upper = 7.5
lower = 7
Integer solution (2, 1)

## Slide 107: One More Example on B&B
upper = 9.25 at (1.75, 1)
upper = 7.0 at (1, 1)
Infeasible
upper = 6 at (2, 0)
x1
x2
0 1 2 3
1
0
upper = 8.67 at (2, 0.67)

## Slide 108: Summary of Branch and Bound
Implicitly enumerate all possible integer solutions
  (R-MILP) is an LP that could be solved by Simplex (or others)
  A child node will always have a worse objective function value  (bounding)
  Search the enumeration tree, but at each node solve the linear program at the node and eliminate the subtree (fathom it) if
    There is no feasible solution or
    The solution is integer (there is no need to go further) or
    The best solution in the subtree cannot be as good as the best available solution
upper = 8.43
upper = 7.5
upper = lower = 7
upper = 6
infeasible

## Slide 109: Overview of Cutting Planes
Try to get better bounds so that more nodes of the branch and bound tree can be fathomed as early as possible
  Recall: we eliminate a node j if the LP bound for j is no more than the upper bound – trying to get a better bound
  Note that a new “cut” removing a corner, and no integer solutions are being excluded
z
feasible
New plane

## Slide 110: Using Cutting Planes
Idea: add constraints that eliminate fractional solutions to the LP without eliminating any integer solutions.
  add “y 1”
  add “y  x –1”
P
x
y
min x + 10y s.t. x, y are in P x, y integer
Optimal fractional (i.e. infeasible solution)
Optimum (integer) solution

## Slide 111: Convex Hull
If we add exactly the right inequalities, then every extreme point of the LP will be integer, and the IP can be solved by solving the LP
We call this minimal LP, the convex hull of the IP solutions.
  For large problems, these constraints are hard to find.
x
y
Optimum (integer) solution
P
min x + 10y s.t. x, y are in P x, y integer

## Slide 112: Motivation for Branch-and-Cut
x1
x2
0 1 2 3
1
0
The tightest possible constraints are called facets
If we have convex hull, we just solve one LP
We need facet defining inequalities
Facet
upper = 9.25 at [1.75, 1]
upper = 7.0 at [1, 1]
Infeasible
upper = 6 at [2, 0]
upper = 8.67 at [2, 2/3]

## Slide 113: Valid Inequalities and Cutting Planes
x1
x2
0 1 2 3
1
0
It is hard to get facet defining inequalities for large problems
We try to approximate by adding valid inequalities
For max. problem, if zLP is the optimum for the LP relaxation, and zIP is the optimum for the IP, then zIP  zLP
Ideally, we want zIP to be as close to zLP as possible
Adding “cuts” can reduce zLP significantly
Valid inequality
Cutting plane
Facet
x1
x2
1
0
0 1 2 3

## Slide 114: Gomory Cuts
Original inequality (ith row):
  All the xj must be integer variables
If all the variables in (1) are non-negative integers then the Gomory Cut is given by:
Can you prove it?

## Slide 115: Gomory Cut Example
For x1 , x2 = 0 or 1
x1 + x2 ≤ 1.5
⇒ x1 + x2 ≤ 1 Cuts-off (0.75, 0.75)
x1 + 0.75 x2 ≤ 2.5
⇒ x1 ≤ 2 Cuts-off (2.5, 0)
1.5 x1 + x2 ≤ 2
⇒ x1 + x2 ≤ 2 Not tighter

## Slide 116: Gomory Cut Example – fractional example
Consider the following constraint in an integer program
1.6 x1 + 4.2 x2 + 3 x3 + 0.4 x4 = 9.8
Focus on the fractions: 1 + 4 + 3 + 0 < 9
⇒ 3/5 x1 + 1/5 x2 +2/5 x4 = Integer + 4/5
⇒ 3/5 x1 + 1/5 x2 + 2/5 x4  4/5
⇒ 3 x1 + x2 + 2 x4  4
x1
x2
x4
x3
1 3/5
4 1/5
2/5
3
=
9 4/5

## Slide 117: Cover Inequalities
Original knapsack inequality:
Let C be a subset of J such that
Then a valid cover inequality is given by:
We have to separate cover inequalities
Example: 5x1 + 6x2 + 7x3 ≤ 10, x1, x2, x3 {0, 1}
  ⇒ x1 + x2 ≤ 1 Cuts-off (1, 0.5, 0), (0.5, 1, 0)
  ⇒ x2 + x3 ≤ 1 Cuts-off (0, 1, 0.5), (0, 0.5, 1)
  ⇒ x1 + x2 + x3 ≤ 1 Yields the Convex Hull

## Slide 118: Example Revisited
maximize 16x1 + 22x2 + 12x3 + 8x4 +11x5 + 19x6
subject to 5x1 + 7x2 + 4x3 + 3x4 +4x5 + 6x6  14
xj = 0, 1 for j = 1 to 6
Exercise: Can you derive some valid cover inequalities?

## Slide 119: After Two Cuts
maximize 16x1 + 22x2 + 12x3 + 8x4 +11x5 + 19x6
subject to 5x1 + 7x2 + 4x3 + 3x4 +4x5 + 6x6  14
x1 + x2 + x6  2
x2 + x3 + x6  2
0  xj  1 for j = 1 to 6
The optimal solution: x1 = 1/3, x2 = 1, x3 = 1/3, x4 = 0, x5 = 0, x6 = 1, z = 44

## Slide 120: More Cuts
x1 + x2 + x6  2
x2 + x3 + x6  2
x1 + x2 + x3  2
x1 + x3 + x6  2
Then we can have
x1 + x2 + x3 + x6  8/3
⇒ x1 + x2 + x3 + x6  2

## Slide 121: Tighter Formulation
Note 1: 43 is the optimal objective value.
Note 2: 1 (or 5) cuts v.s. 25 nodes of a B&B tree
maximize 16x1 + 22x2 + 12x3 + 8x4 +11x5 + 19x6
subject to 5x1 + 7x2 + 4x3 + 3x4 +4x5 + 6x6  14
x1 + x2 + x3 + x6  2
0  xj  1 for j = 1 to 6
The optimal solution:
x1 = 0, x2 = 1, x3 = 0, x4 = 0, x5 = 1/4, x6 = 1, z = 43 3/4
So, z*  43

## Slide 122: Cutting Planes and LP Relaxation
Start with an integer program with integer coefficients and integer right-hand sides, and all variables are constrained to be integer.
Solve the current LP relaxation in standard form. Identify a basic variable that is not integer in the current LP optimal solution.
Identify a row of the optimal tableau corresponding to this fractional variable, such that (right hand side) is fractional. If N denote the set of non-basic variables, this row in the optimal tableau is given by:
Add the following cutting plane to the current LP.
Repeat steps 2-4 until the resulting optimal LP solution is integer; this solution is then an optimal solution to the original integer program.

## Slide 123: Cutting Planes and LP Relaxation
Example: Consider the following Integer Program and its Linear Program relaxation (in standard form)
LP relaxation gives (x1 = 1.5, x2 = 2.5), which is not integer
Pick a ‘row’ from LP relaxation that rhs is not integer
e.g. x2 + 0.1x3 + 0.1x4 = 2.5
Derive a Gomory cut as: x2 ≤ 2

## Slide 124: Cutting Planes and LP Relaxation
Example: The updated Linear Program relaxation with the cut of (in standard form)
LP relaxation gives (x1 = 0.75, x2 = 2), which is not integer
Pick a ‘row’ from LP relaxation that rhs is not integer
e.g. x1- 0.25 x3+1.5x5 = 0.75
Derive a Gomory cut as: x1- x3+x5 ≤ 0
Add this cut and solve the updated LP, we get (x1 = 1, x2 = 2), which is the optimal (and integer) solution.

## Slide 125: Branch-and-Cut – Closing the Gap “Faster”
Presolving
Node Selection
Node Presolve
LP Relaxation
Heuristics
Branching
Cutting Plane
Gomory Cuts
(0-1/2) Cuts
Disjunctive Cuts
Flow Covers
MIR Cuts
…
Heuristics
Local Branching
Feasibility Pump
Relaxation Induced Neighborhood Search
…
Tighten formulation
Reduce problem size

## Slide 126: Modeling of Boolean Expressions
Literal in propositional logic
  Pi TRUE yi =1
  ┐Pi FALSE yi =0
  Example Pi: select equipment/pipe size I
  Using binary variable yi=0,1 for Pi, i.e. yi =1 TRUE, yi =0 FALSE
Set of literals Pi by OR (˅), AND (˄), IMPLICATION ()
Representation linear 0-1 inequalities
  ASSIGN binary variable yi to Pi (1 – yi) to ¬ Pi
  OR P1 ∨ P2 ∨…∨ Pn y1 + y2 + .. + yn ≥ 1
  AND P1 ∧ P2 ∧…∧ Pn y1 ≥ 1, y2 ≥ 1, …yn ≥ 1
  IMPLICATION P1 ⇒ P2 EQUIVALENT TO ¬ P1 ∨ P2
    i.e. 1 – y1 + y2 ≥ 1 OR y2 ≥ y1

## Slide 127: Show that y1 ⇒ y2 is equivalent to ¬ y1 ∨ y2
y1 | y2 | y1 ⇒ y2 | ¬ y1 | ¬ y1 ∨ y2
1 | 1 | 1 | 0 | 1
1 | 0 | 0 | 0 | 0
0 | 1 | 1 | 1 | 1
0 | 0 | 1 | 1 | 1

## Slide 128: De Morgan’s Theorem and CNF
De Morgan’s Theorem
  ¬ (P1 ∧ P2) ⇔ ¬ P1 ∨ ¬ P2
  ¬ (P1 ∨ P2) ⇔ ¬ P1 ∧ ¬ P2
Conjunctive Normal Form (CNF)
  Logic expressions composed by AND with OR inside
  Q1 ∧ Q2 ∧ . . . ∧ Qs
  where clause Qi : P1 ∨ P2 ∨ . . . ∨ Pr (Note: all OR)
  Example: (P1 ∨ ¬ P2) ∧ (¬ P2 ∨ P3) is equivalent to
  y1 + 1 – y2 ≥ 1, 1 – y2 + y3 ≥ 1

## Slide 129: Linear Inequalities for Logic Propositions
Goal is to Convert Logical Expression into CNF
BASIC STEPS
Step 1. Replace implication by disjunction
  P1 ⇒ P2 ⇔ ¬ P1 ∨ P2
Step 2. Move negation inward applying de Morgan’s theorem
  ¬ (P1 ∧ P2) ⇔ ¬ P1 ∨ ¬ P2
  ¬ (P1 ∨ P2) ⇔ ¬ P1 ∧ ¬ P2
Step 3. Recursively distribute OR over AND
  (P1 ∧ P2) ∨ P3 ⇔ (P1 ∨ P3) ∧ (P2 ∨ P3)

## Slide 130: Example
Product recovery: if the absorber or the membrane separator is selected, then do not use cryogenic separation.
Assigning the boolean literals to each action
  PA = select absorber
  PM = select membrane separator
  PC = select cryogenic separation
  Logic Expression: PA ∨ PM ⇒ ¬ PC
  Removing the implication: ¬ (PA ∨ PM ) ∨ ¬ PC
  De Morgan’ Theorem: (¬ PA ∧ ¬ PM ) ∨ ¬ PC
  Moving Or over the AND: (¬ PA ∨ ¬ PC) ∧ (¬ PM ∨ ¬ PC)
    1 – yA + 1 – yC ≥ 1, 1 – yM + 1 – yC ≥ 1
    yA + yC ≤ 1, yM + yC ≤ 1

## Slide 131: Example
flash ⇒ distillation ∨ absorption
  PF ⇒ PD ∨ PA
  ¬ PF ∨ PD ∨ PA remove implication
  1 – yF + yD + yA ≥ 1 all y = 0, 1
  yD + yA ≥ yF
membrane ⇒ not absorption ∧ compressor
  PM ⇒ ¬ PA ∧ PC
  ¬ PM ∨ (¬ PA ∧ Pc) remove implication
  (¬ PM ∨ ¬ PA) ∧ (¬ PM ∨ Pc) distribute OR over AND ⇒ CNF!
  1 – yM + 1 – yA ≥ 1 1 – yM + yC ≥ 1 all y = 0, 1
  yM + yA ≤1 yC ≥ yM

## Slide 132: Example
  (P1 ∧ P2) ∨ P3 ⇒ (P4 ∨ P5 )
  Removing the implication, the above proposition yields:
  ¬ [ (P1 ∧ P2) ∨ P3 ] ∨ P4 ∨ P5
  Moving the negative inwards leads to the following steps
  [¬ (P1 ∧ P2) ∧ ¬ P3 ] ∨ P4 ∨ P5
  [ (¬ P1 ∨ ¬ P2) ∧ ¬ P3 ] ∨ P4 ∨ P5
Recursively distributing the ‘OR’ over the ‘AND’
  (¬ P1 ∨ ¬ P2 ∨ P4 ∨ P5) ∧ (¬ P3 ∨ P4 ∨ P5) (CNF)

## Slide 133: Exercise
The following conditions arise in the context of a problem synthesis problem:
If x is true and y is true, then z is true
If x is true or y is false, then w is false
If both z and w are false, then x and/or y should be true
Formulate linear inequalities in terms of 0-1 variables to model the above conditions

## Slide 134: Example: Integer Cut
The choice of all 0-1 combinations for yj, j∈J is feasible, except the one for which yj = 0, j ∈ N, yj = 1, j ∈ B, where N and B are specified partitions of J.

## Slide 135: Example: Multiperiod Problems
“If Task yi is performed in any time period i = 1, ..n select Unit z”
Intuitive Approach
y1 + y2 + . . . + yn ≤ n*z (1)
Logic Based Approach
y1 ∨ y2 ∨ . . . ∨ yn ⇒ z
  ¬(y1 ∨ y2 ∨ . . . ∨ yn) ∨ z
  (¬ y1 ∨ z) ∧ (¬ y2 ∨ z) ∧ . . . ∧ (¬ yn ∨ z)
  1 – y1 + z ≥ 1, 1 – y2 + z ≥ 1, …, 1 – yn + z ≥ 1
y1 ≤ z, y2 ≤ z, … , yn ≤ z (2)
Inequalities (2) are stronger than inequalities (1)

## Slide 136: Geometrical Interpretation
y1 ≤ z
y2 ≤ z
y1 + y2 ≤ 2z
All extreme points in hypercube are integer!
Non-integer extreme points Weaker relaxation!
y2
y1
z
1
1
1
y2
y1
z
1
1
1
0.5
0.5

## Slide 137: Disjunctive Programming
We may want to enforce different conditions in different cases
  Examples: Selection of reactor type
  Selection of an additional flash tank
To find the optimal design we need to handle the following logic constraints:
  We have to convert the disjunction into MIP constraints, handled by MIP solvers

## Slide 138: Disjunctions
How to model the following constraint:
f1(x) ≤ 0 OR f2(x) ≤ 0
  This is called ‘disjunction’. We can model it by introducing binary variables y (or y1 and y2):
  where M1, M2 are sufficiently large numbers
The disjunction form is given below:

## Slide 139: Big-M Reformulation
Selecting : M = 7

## Slide 140: Convex Hull Reformulation

## Slide 141: Modeling of Disjunctions
Disjunctions: one inequality must be hold
Big-M Formulation
Difficulty: Parameter Mi
  Must be sufficiently large to render inequality redundant
  Large value yields poor relaxation

## Slide 142: Convex-Hull Formulation (Balas, 1985)
Disaggregate variables
(may be removed)
Disjunctions
Convex-hull Formulation

## Slide 143: Proof
Nonlinear disj. equiv.

## Slide 144: Example
Big-M formulation
Convex-hull formulation
Disjunctions

## Slide 145: Exercise
Reformulate the following problem as an MILP using the convex hull formulation

## Slide 146: MILP Solvers
Primary MIP solvers: CPLEX, GUROBI, FICO-Xpress
  GUROBI: Zhonghao Gu, Ed Rothberg, Bob Bixby
Other commercial solvers: Mosek, …
Free/Open-source Solvers: SCIP, MIP-CL, CBC

## Slide 147: MIP Solver Benchmark (April 2017)
MIP solver benchmark (1 thread): Unsolved or failed instances are accounted for with the time limit of 2 hours.
  Commercial solvers remain 6-7 times faster than these free/open-source ones

## Slide 148: MIP Computational History: 1950 - 1998
1954: Dantzig, Fulkerson, S. Johnson: 42 city TSP
1957: Gomory, cutting plane algorithm
1960: Land, Doig
1965: Dakin, Branch-and-bound (B&B)
1971: MPSX/370, Benichou et al.
1972: UMPIRE, Forrest, Hirst, Tomlin
1972 – 1998: Good B&B remained the state-of-the-art in commercial codes, in spite of
  1973 Padberg
  1974 Balas (disjunctive programming)
  1983 Crowder, Johnson, Padberg: PIPX, pure 0/1 MIP
  1987 Van Roy and Wolsey: MPSARX, mixed 0/1 MIP
  Grötschel, Padberg, Rinaldi…TSP

## Slide 149: MIP Computational History: 1998 – 2017
Linear programming
  Stable, robust dual simplex
Variable/node selection
  Influenced by traveling salesman problem
Primal heuristics
  Construction & improvement heuristics; neighbor search
Presolve
  Fast, incremental bound strengthening
Cutting planes
  Cliques, disjunctive, flow covers, Gomory, GUB covers, knapsack covers, implied bounds, mix-integer rounding, path cuts, etc.
  Aggregation
  …

## Slide 150: Progress in Mixed-Integer Linear Programming
2,856 binary variables, 25,755 variables, 48,939 constraints
  Unit Commitment: California 7-Day Model
1999 1 hr initial LP, unfinished after 8 hours
2010 Gurobi 3.0: 195 seconds
=> 80,000 speed-up!!

## Slide 151: MIP Computational History: 1988 – 2017
Improvement in MIP Software from 1988-2017
Algorithms: 147,650×
Machines: 17,120×
  http://preshing.com/20120208/a-look-back-at-single-threaded-cpu-performance/
NET: (Algorithm × Machine): 2,527,768,000×
Example of implication
A “typical" MILP that would have taken 124 years to solve in 1988 will solve in 1 second in 2017.

## Slide 152: From Bixby, Rothberg and Gu (2009)

## Slide 153: From Bixby, Rothberg and Gu (2009)

## Slide 154: Solving MILP with GAMS
Declare integer or binary (0-1) variables
  Binary variable VARIABLE_NAME;
Optimality gap
  GAMS default is 10%, i.e. optcr = 0.1. To set the optimality gap for branch-and-bound to zero, type the following line:
    Option optcr = 0;

## Slide 155: Solving MILP with PYOMO